## Slide 1: Lake Elsinore and Canyon Lake TMDL Water Quality Monitoring Update – 2016-17 Summary
August 15, 2017

## Slide 2: Lake Elsinore and Canyon Lake TMDL Water Quality Monitoring Update – 2016-17 Summary
Watershed Monitoring

## Slide 3: Summary of 2016-2017 Watershed Monitoring and Nutrient Loads
Number and Location Description | Annual Flow (Mgal) | Annual Event Mean Storm Concentration (mg/L) |  | Estimated Annual Load (kg) | 
 |  | Total Nitrogen | Total Phosphorus | Total Nitrogen | Total Phosphorus
Site 3 - Salt Creek at Murrieta Road | 1,596 | 2.07 | 0.62 | 12,366 | 4,026
Site 4 - San Jacinto River at Goetz | 2,802 | 2.03 | 1.23 | 21,651 | 14,403
Site 6 - San Jacinto River at Ramona Expressway | 0 | - | - | - | -
Site 30 - Canyon Lake Spillway | 4,850 | 1.85 | 0.36 | 33,759 | 6,637
Site 1 - San Jacinto River at Cranston Guard Station | 6,194 | Not Measured | Not Measured | Not Measured | Not Measured

## Slide 4: Summary of 2016-2017 Monthly Flow
Mean Monthly Flow (cfs) | Site 3 - Salt Creek | Site 4 - San Jacinto River | Site 6 - San Jacinto River at Ramona Expressway | Site 30 - Canyon Lake Spillway | Site 1 - San Jacinto River at Cranston Guard Station
July | 0.00 | 0.00 | - | 3.10 | 0.05
August | 0.00 | 0.00 | - | 2.89 | 0.03
September | 0.00 | 0.00 | - | 0.16 | 0.01
October | 0.17 | 0.00 | - | 0.15 | 0.02
November | 3.67 | 3.01 | - | 0.67 | 0.05
December | 23.51 | 32.95 | - | 25.80 | 14.41
January | 43.55 | 90.61 | - | 176.06 | 72.75
February | 9.01 | 14.48 | - | 25.04 | 125.53
March | 0.73 | 0.31 | - | 6.39 | 86.86
April | 0.00 | 0.00 | - | 1.03 | 15.60
May | 0.00 | 0.00 | - | 2.98 | 5.71
June | 0.00 | 0.00 | - | 0.27 | 0.84
Mean Annual Flow (cfs) | 6.98 | 12.26 | - | 20.56 | 27.77

## Slide 5: Summary of 2016-2017 Rainfall
Monthly Rainfall (inches) | Lake Elsinore | Perris CDF | Pigeon Pass | Hemet / San Jacinto | Winchester
Jul | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Aug | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Sep | 0.08 | 0.08 | 0.00 | 0.16 | 0.12
Oct | 0.24 | 0.35 | 0.78 | 0.34 | 0.28
Nov | 0.98 | 0.90 | 1.35 | 1.09 | 1.03
Dec | 3.60 | 3.21 | 3.94 | 3.20 | 3.17
Jan | 6.68 | 6.04 | 6.78 | 6.23 | 4.86
Feb | 3.02 | 2.06 | 2.61 | 2.86 | 2.31
Mar | 0.03 | 0.02 | 0.16 | 0.21 | 0.06
Apr | 0.02 | 0.00 | 0.02 | 0.00 | 0.00
May | 0.27 | 0.06 | 0.26 | 0.25 | 0.08
Jun | 0.00 | 0.00 | 0.00 | 0.00 | 0.02
Annual Rainfall (Inches) | 14.92 | 12.72 | 15.90 | 14.34 | 11.93

## Slide 6: 2016-2017 Annual Hydrograph

## Slide 7: 2016-2017 Annual Hydrograph

## Slide 8: 2016-2017 Annual Hydrograph

## Slide 9: 2016-2017 Annual Hydrograph

## Slide 10: 2016-2017 Annual Hydrograph

## Slide 11
Wet Event #1
December 16-18, 2016
Rainfall: 0.43 to 0.78 inches
Sites: Salt Creek and San Jacinto

## Slide 12
Wet Event #2
January 19-22, 2017
Rainfall: 1.32 to 2.0 inches
Sites: Salt Creek, San Jacinto, and Canyon Lake

## Slide 13
Wet Event #3
February 17-20, 2017
Rainfall: 0.97 to 1.66 inches
Sites: Salt Creek, San Jacinto, and Canyon Lake

## Slide 14: Summary of 2008-2017 Nutrient Concentrations
Monitoring Year | Site 3 - Salt Creek |  | Site 4 - San Jacinto River |  | Site 30 - Canyon Lake Spillway | 
 | TN (mg/L) | TP (mg/L) | TN (mg/L) | TP (mg/L) | TN (mg/L) | TP (mg/L)
2008-2009* | 3.0/3.1 | 0.8/1.3 | 1.4/3.1 | 0.7/1.5 | NS | NS
2009-2010* | 1.5/1.9 | 0.6/1.0 | 1.6/3.2 | 0.5/1.2 | 0.7/1.3 | 0.6/0.8
2010-2011* | 1.5/2.2 | 0.4/0.5 | 1.4/2.2 | 0.7/1.9 | 0.9/1.5 | 0.5/0.9
2011-2012 | 1.9 | 0.3 | 2.2 | 0.5 | NS | NS
2012-2013 | 1.9 | 0.3 | 2.1 | 0.5 | NS | NS
2013-2014 | 2.7 | 0.9 | 1.8 | 0.6 | NS | NS
2014-2015 | 2.2 | 0.5 | 1.8 | 0.4 | NS | NS
2015-2016 | 2.5 | 0.5 | 2.4 | 1.4 | NS | NS
2016-2017 | 2.1 | 0.6 | 2.0 | 1.2 | 1.9 | 0.4
*Values shown for nutrient concentrations are minimum/maximum NS-Not sampled |  |  |  |  |  | 

## Slide 15: Summary of 2008-2017 Nutrient Loads
Monitoring Year | Site 3 - Salt Creek |  |  | Site 4 - San Jacinto River |  |  | Site 30 - Canyon Lake Spillway |  | 
 | Flow (Mgal) | TN (kg) | TP (kg) | Flow (Mgal) | TN (kg) | TP (kg) | Flow (Mgal) | TN (kg) | TP (kg)
2008-2009* | 529 | 6,085/6,125 | 1,541/2,642 | 1,042 | 5,323/12,145 | 2,682/5,954 | NA | NS | NS
2009-2010* | 1,282 | 7,474/9,180 | 2,960/4,804 | 2,681 | 14,716/32,680 | 4,668/12,382 | 62 | 167/294 | 137/188
2010-2011* | 1,946 | 5,112/7,484 | 1,370/1,704 | 3,269 | 7,690/12,124 | 4,041/10,664 | 1,302 | 2,035/3,556 | 1,029/2,102
2011-2012 | 249 | 1,843 | 238 | 277 | 2,338 | 542 | 133 | NS | NS
2012-2013 | 147 | 1,025 | 180 | 424 | 3,341 | 822 | 114 | NS | NS
2013-2014 | 411 | 4,268 | 1,409 | 484 | 3,252 | 1,178 | 148 | NS | NS
2014-2015 | 511 | 4,661 | 1,257 | 570 | 3,932 | 1,041 | 196 | NS | NS
2015-2016 | 515 | 5,647 | 1,447 | 872 | 7,926 | 4,624 | 476 | NS | NS
2016-2017 | 1,596 | 12,366 | 4,026 | 2,802 | 21,651 | 14,403 | 4,850 | 33,759 | 6,637
*Values shown for nutrient loads are minimum/maximum NS-Not Sampled NA-Not Available |  |  |  |  |  |  |  |  | 

## Slide 16: Lake Elsinore and Canyon Lake TMDL Water Quality Monitoring Update – 2016-17 Summary
In-Lake Monitoring

## Slide 17: Station Locations – Lake Elsinore

## Slide 18: Station Locations – Canyon Lake

## Slide 19: Total Nitrogen – Lake Elsinore 2016-2017

## Slide 20: Total Nitrogen – Lake Elsinore Historic Data

## Slide 21: Total Phosphorus – Lake Elsinore 2016-2017

## Slide 22: Total Phosphorus – Lake Elsinore Historic Data

## Slide 23: Total Dissolved Solids– Lake Elsinore 2016-2017

## Slide 24: Total Dissolved Solids– Lake Elsinore Historic Data

## Slide 25: Total Nitrogen – Canyon Lake 2016-2017

## Slide 26: Total Nitrogen – Canyon Lake Historic Data

## Slide 27: Total Phosphorus – Canyon Lake 2016-2017

## Slide 28: Total Phosphorus – Canyon Lake Historic Data

## Slide 29: Satellite Imagery – Chlorophyll July 2016
Lake Elsinore
Canyon Lake
**Data gaps in eastern arm due to high cirrus clouds

## Slide 30: Satellite Imagery – Chlorophyll August 2016
Lake Elsinore
Canyon Lake
**Data gaps due to large floating cyanobacterial slicks

## Slide 31: Satellite Imagery – Chlorophyll September 2016
Lake Elsinore
Canyon Lake
**Data gaps due to large floating cyanobacterial slicks

## Slide 32: Satellite Imagery – Chlorophyll October 2016
Lake Elsinore
Canyon Lake
**Data gaps in eastern arm due to high cirrus clouds

## Slide 33: Satellite Imagery – Chlorophyll December 2016
Lake Elsinore
Canyon Lake
**Data gaps due to large floating cyanobacterial slicks

## Slide 34: Satellite Imagery – Chlorophyll February 2017
Lake Elsinore
Canyon Lake
**High chlorophyll-a readings in Canyon Lake due to turbidity interference

## Slide 35: Satellite Imagery – Turbidity after January Storms
Canyon Lake

## Slide 36: Satellite Imagery – Chlorophyll April 2017
Lake Elsinore
Canyon Lake

## Slide 37: Satellite Imagery – Chlorophyll June 2017
Lake Elsinore
Canyon Lake

## Slide 38: Lake Elsinore Chlorophyll – 2016-2017

## Slide 39: Lake Elsinore Chlorophyll – Integrated Historic Data

## Slide 40: Canyon Lake Chlorophyll – 2016-2017

## Slide 41: Canyon Lake Chlorophyll – Integrated Historic Data

## Slide 42: Lake Elsinore and Canyon Lake TMDL Water Quality Monitoring Update – 2016-17 Summary
Dissolved Oxygen Monitoring

## Slide 43: Lake Elsinore Dissolved Oxygen – LE02 Water Column Mean vs. 1m from Bottom 2016-2017

## Slide 44: Lake Elsinore Dissolved Oxygen – LE02 Water Column Mean Historic Data

## Slide 45: Lake Elsinore Dissolved Oxygen – LE02 1m from Bottom Historic Data

## Slide 46: Canyon Lake Dissolved Oxygen – Main Basin Epilimnion vs. Hypolimnion 2016-2017
No stratification in December-February
Not sampled in July 2016
Mean of Sites CL07 & CL08

## Slide 47: Canyon Lake Dissolved Oxygen – East Basin Epilimnion vs. Hypolimnion 2016-2017
No stratification in Sept (CL10) & Dec/Feb (both)
Not sampled in July 2016
Mean of Sites CL09 & CL10

## Slide 48: Dissolved Oxygen – Diurnal Variability

## Slide 49: Lake Elsinore Dissolved Oxygen – Morning vs. Afternoon TMDL Compliance July 2015 to June 2017
Site | TMDL DO Target | Time of Measurement | # of Events | # Events in Compliance | Percent of Events in Compliance
LE01 | 2015 Water Column Mean | Morning | 14 | 9 | 64%
 |  | Afternoon | 13 | 10 | 77%
 | 2020 1m from Bottom | Morning | 14 | 6 | 43%
 |  | Afternoon | 13 | 5 | 38%
LE02 | 2015 Water Column Mean | Morning | 14 | 7 | 50%
 |  | Afternoon | 13 | 9 | 69%
 | 2020 1m from Bottom | Morning | 14 | 7 | 50%
 |  | Afternoon | 13 | 5 | 38%
LE03 | 2015 Water Column Mean | Morning | 14 | 9 | 64%
 |  | Afternoon | 14 | 10 | 71%
 | 2020 1m from Bottom | Morning | 14 | 7 | 50%
 |  | Afternoon | 14 | 7 | 50%

## Slide 50: Lake Elsinore Dissolved Oxygen – Morning vs. Afternoon TMDL Compliance by Season July 2015 to June 2017
Plotting mean difference in Morning vs. Afternoon DO values
* = Statistically Significant Morning vs. Afternoon
Note: Positive values represent periods when DO increased from morning to afternoon, negative values indicate a decrease in DO from morning to afternoon

## Slide 51: Canyon Lake Dissolved Oxygen – Morning vs. Afternoon TMDL Compliance July 2015 to June 2017
Site | TMDL DO Target | Time of Measurement | # of Events | # Events in Compliance | Percent of Events in Compliance
CL07 | 2015 Epilimnion | Morning | 11 | 10 | 91%
 |  | Afternoon | 9 | 9 | 100%
 | 2020 Hypolimnion | Morning | 11 | 0 | 0%
 |  | Afternoon | 9 | 0 | 0%
CL08 | 2015 Epilimnion | Morning | 11 | 11 | 100%
 |  | Afternoon | 9 | 9 | 100%
 | 2020 Hypolimnion | Morning | 11 | 1 | 9%
 |  | Afternoon | 9 | 2 | 22%
CL09 | 2015 Epilimnion | Morning | 11 | 11 | 100%
 |  | Afternoon | 9 | 9 | 100%
 | 2020 Hypolimnion | Morning | 11 | 2 | 18%
 |  | Afternoon | 9 | 1 | 11%
CL10 | 2015 Epilimnion | Morning | 8 | 8 | 100%
 |  | Afternoon | 8 | 8 | 100%
 | 2020 Hypolimnion | Morning | 7 | 3 | 43%
 |  | Afternoon | 8 | 5 | 63%
Note: Only events shown are those when thermal stratification was present at the time of monitoring.
No measurements were taken in the afternoon for October 2015 or September 2016 events.

## Slide 52: Canyon Lake Dissolved Oxygen – Morning vs. Afternoon TMDL Compliance by Season July 2015 to June 2017
Plotting mean difference in Morning vs. Afternoon DO values
* = Statistically Significant Morning vs. Afternoon
Note: Positive values represent periods when DO increased from morning to afternoon, negative values indicate a decrease in DO from morning to afternoon
No difference in mean DO was observed between morning and afternoon in epilimnion or hypolimnion at Site CL07 during summer periods

## Slide 53: Lake Elsinore Dissolved Oxygen Do In-Lake Sondes Represent Lake-wide Conditions?
Data points represent individual 1-m depth readings
Hand-held meter readings were taken immediately adjacent to in-lake sondes with maximum 30-minute time difference
Hand-held Profiles vs. In-lake Sondes July 2015 to June 2017

## Slide 54: Lake Elsinore Dissolved Oxygen – July 2015 to June 2017 Do In-Lake Sondes Represent Lake-wide Conditions?
Hand-held meter and In-lake sonde in general agreement
Hand-held meter and In-lake sonde not in agreement
Grand Avenue Sonde
Data points represent water column means

## Slide 55: Lake Elsinore and Canyon Lake TMDL Water Quality Monitoring Update – 2016-17 Summary
Cyanobacterial Toxin Monitoring

## Slide 56: Lake Elsinore Cyanotoxin Bloom Water Samples 2016-2017

## Slide 57: Lake Elsinore Cyanotoxin Bloom Scum Samples 2016-2017

## Slide 58: Satellite Imagery Cyanotoxin Indicator – July 2017

## Slide 59: Questions?

## Slide 60: Back Up Slides

## Slide 61: Cyanotoxin Concentrations– Lake Elsinore 2016-2017
Analytes | Microcystin Concentration (ug/L) |  |  |  |  |  |  |  |  |  | 
 | July 27 | Aug 1 | Aug 9 | Aug 18 | Aug 29 | Sept 19 | Oct 5 | Dec 8 | Feb 2 | Apr 7 | Jun 2
La Laguna Boat Ramp - Scum | 26500 |  | 19450 | 382 | 26000 | 23425 | 6600 | 201 |  |  | 
La Laguna Boat Ramp - Surface Water | 5.36 |  | 11.6 | 77.5 | 5950 | 27.5 | 19.4 |  | 2.35 | 4.19 | 
Center Lake - Depth Integrated Water |  | 5.3 | 8.9 | 7.2 | 30.6 | 13.5 | 20 |  |  |  | 1.4
Center Lake - Scum |  | 93500 |  |  |  | 3110 | 70 | 114 |  |  | 
Center Lake - Surface Water |  |  | 161 | 10.6 | 15.3 |  |  |  | 1.59 | 3.87 | 1.2
Elm Grove Beach - Surface Water |  |  | 326 | 163 | 172 | 10900 | 35 | 56 | 2.79 | 2.7 | 
California CyanoHAB Trigger Levels for Human Health (ug/L) |  |  | 
Toxin | Caution – Action Trigger | Warning – Tier 1 | Danger – Tier 2
Microcystin | 0.8 | 6.0 | 20